## Slide 1
Digital Design and Computer Architecture | Group Project Presentation
Student Name | Roll No.
STUDENT NAME | ROLL NO.
STUDENT NAME | ROLL NO.
STUDENT NAME | ROLL NO.
STUDENT NAME | ROLL NO.

## Slide 2
DIGITAL DESIGN AND COMPUTER ARCHITECTURE
4-bit Binary-to-Decimal Conversion and Display System
Designed with logic gates, from switches to 7-segment displays, and linked to a RISC-V processor
K-maps
7-segment
CO1 to CO6
4 Parts | Input to Display

## Slide 3
OVERVIEW
Project Division and Course Outcomes
3
Each part hands its outputs to the next.
Part | Topic | Outcomes
Part 1 | Foundations: problem, number systems, truth table, gates | CO1
Part 2 | Binary to BCD with K-maps | CO2
Part 3 | 7-segment decoder, display control, ROM version | CO2, CO3, CO4
Part 4 | RISC-V view, peripheral integration, results | CO5, CO6

## Slide 4
OVERVIEW
Where Each Course Outcome Appears
4
All six course outcomes are used in the project.
CO | Outcome | Used in this project
CO1 | Binary, digital representation, logic gates | Truth table, gate toolkit, NAND (Part 1)
CO2 | Combinational logic, K-maps, adders and ALU | BCD and segment equations, +6 adder idea (Parts 2, 3)
CO3 | Flip-flops, counters, FSMs | Input register, display multiplexing FSM (Part 3)
CO4 | Register file and memory | ROM-based segment decoder (Part 3)
CO5 | RISC-V execution, datapath, control | Assembly version of the conversion (Part 4)
CO6 | Architectural extension, peripherals | Memory-mapped converter peripheral (Part 4)

## Slide 5
PART 1 | CO1
Problem Statement and Block Diagram
5
Input switches A B C D, with A as the most significant bit.
THE PROBLEM
Show a 4-bit binary number as a readable decimal number, using logic gates.
THE GOAL
A working circuit that displays 00–15 on two 7-segment displays.
Input
Switches A B C D
>
Binary to BCD
K-map logic (Part 2)
>
Decode
BCD to 7-segment (Part 3)
>
Display
Two 7-segment digits
TWO-DIGIT OUTPUT
Tens digit T (0 or 1) drives the left display; units U3–U0 drive the right display

## Slide 6
PART 1 | CO1
Number Systems and Truth Table
6
T = tens digit. Units digit is N for 0–9 and N − 10 for 10–15.
Dec | B3B2B1B0 | T | U3U2U1U0
0 | 0000 | 0 | 0000
1 | 0001 | 0 | 0001
2 | 0010 | 0 | 0010
3 | 0011 | 0 | 0011
4 | 0100 | 0 | 0100
5 | 0101 | 0 | 0101
6 | 0110 | 0 | 0110
7 | 0111 | 0 | 0111
Dec | B3B2B1B0 | T | U3U2U1U0
8 | 1000 | 0 | 1000
9 | 1001 | 0 | 1001
10 | 1010 | 1 | 0000
11 | 1011 | 1 | 0001
12 | 1100 | 1 | 0010
13 | 1101 | 1 | 0011
14 | 1110 | 1 | 0100
15 | 1111 | 1 | 0101

## Slide 7
PART 1 | CO1
Logic Gates and NAND Universality
7
Any circuit can be built from one gate type.
Gates and laws
AND, OR, NOT, NAND, NOR, XOR with truth tables
De Morgan: (AB)' = A' + B'
De Morgan: (A+B)' = A'B'
Absorption and consensus for simplification
NAND only
NOT A' = (A·A)'
AND AB = ((AB)')'
OR A+B = (A'·B')'
Two-level NAND-NAND replaces AND-OR.

## Slide 8
PART 2 | CO2
Binary to BCD: Method
8
One 4-variable K-map per output: T, U3, U2, U1, U0.
Approach
Tens digit T is 1 only for 10–15
Units digit is N for 0–9, N − 10 for 10–15
Five outputs from four inputs
Group 1s in powers of two
Reading a K-map
Place the 1s from the truth table
Larger groups give fewer literals
Each group becomes a product term
OR the terms for the output
LINK TO THE ALU
Units digit can also come from an adder: units = N + 6 (mod 16) when N ≥ 10, reusing the ripple-carry adder.

## Slide 9
PART 2 | CO2
Worked K-map: Units Bit U1
9
U1 = 1 for N = 2, 3, 6, 7, 12, 13.
B3B2 \ B1B0 | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 1
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 0 | 0
10 | 0 | 0 | 0 | 0
Groups
Group 1 (N=2,3,6,7): B3'·B1
Group 2 (N=12,13): B3·B2·B1'
U1 = B3'·B1 + B3·B2·B1'

## Slide 10
PART 2 | CO2
Final Equations and Gate Implementation
10
Next: Part 3. T and U3–U0 go in as BCD digits.
Minimised outputs (B3 is MSB)
T = B3·B2 + B3·B1
U3 = B3·B2'·B1'
U2 = B3'·B2 + B3·B2·B1
U1 = B3'·B1 + B3·B2·B1'
U0 = B0
Implementation
AND gates feeding an OR gate per output
NAND-only: each AND-OR becomes NAND-NAND
U0 is a wire from B0
T = 1 exactly for 10–15

## Slide 11
PART 3 | CO2
Segment Truth Table (Common-Cathode)
11
Segment on with logic 1. Inputs 10–15 are don't-cares.
Digit | ABCD | a | b | c | d | e | f | g
0 | 0000 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0001 | 0 | 1 | 1 | 0 | 0 | 0 | 0
2 | 0010 | 1 | 1 | 0 | 1 | 1 | 0 | 1
3 | 0011 | 1 | 1 | 1 | 1 | 0 | 0 | 1
4 | 0100 | 0 | 1 | 1 | 0 | 0 | 1 | 1
5 | 0101 | 1 | 0 | 1 | 1 | 0 | 1 | 1
6 | 0110 | 1 | 0 | 1 | 1 | 1 | 1 | 1
7 | 0111 | 1 | 1 | 1 | 0 | 0 | 0 | 0
8 | 1000 | 1 | 1 | 1 | 1 | 1 | 1 | 1
9 | 1001 | 1 | 1 | 1 | 1 | 0 | 1 | 1

## Slide 12
PART 3 | CO2
Segment Equations
12
Invert every output for a common-anode display.
Minimised with K-maps (A = MSB)
a = A + C + BD + B'D'
b = B' + C'D' + CD
c = B + C' + D
d = A + B'D' + B'C + CD' + BC'D
e = B'D' + CD'
f = A + C'D' + BC' + BD'
g = A + BC' + B'C + CD'
Notes
Active-high outputs
One decoder per digit
Series resistor on each segment

## Slide 13
PART 3 | CO3
Input Register and Display Control
13
Sequential logic added around the combinational core.
Input register
Four D flip-flops store A B C D on the clock edge
Display stays steady while switches change
Same building block as a CPU register
Display multiplexing FSM
Two states: TENS and UNITS
A 1-bit counter toggles each clock
A 4-bit 2:1 MUX picks T or U3–U0
RESULT
One decoder serves both displays; the FSM state enables one digit at a time, saving a decoder.

## Slide 14
PART 3 | CO4
ROM-Based Segment Decoder
14
Memory can replace the decoder gates.
ROM contents: digit to abcdefg
0 -> 1111110
1 -> 0110000
2 -> 1101101
3 -> 1111001
4 -> 0110011
5 -> 1011011
6 -> 1011111
7 -> 1110000
8 -> 1111111
9 -> 1111011
Gates vs memory
A 16 × 7 ROM: address is the BCD digit, data is the segments
Only 10 of 16 addresses are used
Gates: smaller and faster
ROM: patterns are easy to change
Same lookup idea as instruction memory

## Slide 15
PART 4 | CO2 to CO4
Integration and Simulation
15
Simulator: Logisim, Multisim or Proteus.
Build
Switches feed the input register
Binary-to-BCD block, then two decoders
Optional: multiplexed single decoder
Probes on every interface
Live demo
Switch through 0, 5, 9, 10 and 15
Both displays update together
Note propagation delay over two gate stages
Count total gates used

## Slide 16
PART 4 | CO5
Software View: RISC-V Assembly
16
Result: a1 = tens, a0 = units.
Binary to decimal, N in a0 (0–15)
li a1, 0 # tens
li t0, 10
blt a0, t0, done # N < 10 ?
addi a0, a0, -10 # units
addi a1, a1, 1 # tens = 1
done:
On the datapath
RV32I has no divide
N ≤ 15 needs one subtract
blt and addi use the ALU
Registers: read two, write one
Control unit decodes each opcode

## Slide 17
PART 4 | CO6
Converter as a Memory-Mapped Peripheral
17
The CPU writes N; the hardware drives the displays.
CPU
sw writes N
>
Address decode
selects peripheral
>
4-bit register
holds N
>
Converter
BCD, decoders, display
Driver code
lui t1, 0x10000
sw a0, 0(t1)
Design notes
Peripheral sits in the I/O address range
Address decoder is plain gates
Register is made of D flip-flops

## Slide 18
PART 4
Test Results
18
Fill in the Observed column from your own simulation.
Input | Binary | Expected | Observed
0 | 0000 | 00 | 
5 | 0101 | 05 | 
9 | 1001 | 09 | 
10 | 1010 | 10 | 
12 | 1100 | 12 | 
15 | 1111 | 15 | 

## Slide 19
PART 4
Conclusion and Future Scope
19
Binary in, decimal out.
Conclusion
K-map-minimised logic converts 4 bits to BCD
Decoders drive the 7-segment displays
Sequential, memory and RISC-V views link it to a CPU
All 16 inputs map to the right output
Limits and next steps
Fixed 4-bit width
Many gates per output
Extend to 8-bit input
Add the peripheral to a full RISC-V CPU

## Slide 20
THANK YOU
Questions?